PORTAMATRICULAS ADAPTABLE A TRIUMPH SPEED TRIPLE 11’

LICENSE SUPPORT ADAPTABLE TO TRIUMPH SPEED TRIPLE 11’

REF:5732N

#### INSTRUCCIONES DE MONTAJE  / INSTRUCTIONS TO ASSEMBLE

- Desmontar el portamatriculas original / Remove the OEM license support.

- Montar los soportes laterales(1) del portamatriculas suministrado usando los tornillos “A” y “B” originales (figura 1) / Mount the side supports (1) suplied of the license support, using the OEM fasteners A and B (see figure 1).

- Colocar en la posición “E” de la tapa (2) suministrada, la tuerca del portamatriculas original. A continuación montar la tapa, usando los tornillos originales en las posiciones “C” y “D” (figura 2) / Place the nut of the OEM support on the position E of the cover (2) supplied (see figure 2). Next, mount the cover using the OEM fasteners on position C and D (see figure 2).

- Montar la tapa de plástico original, usando el tornillo original “F” (figura 3). A continuación montar el resto de los plásticos de la motocicleta /  Mount the OEM plastic cover using the OEM fastener F (see figure 3). Next, mount the rest of the plastic parts of the motorcycle.

- Se suministran 4 bridas de plàstico(10) para fijar los cables de la instalación eléctrica / Four plastic ziptides (10) are supplied to tight the electric cables.

Material sumistrado para el montaje en la motocicleta:

Material supplied to assemble the license support:

| POSICIÓN | DENOMINACIÓN | CANTIDAD |
| --- | --- | --- |
| 1 | Soportes laterales y central c/negro | Black side and central support | 1 |
| 2 | Tapa c/negro | Black cover | 1 |
| 3 | Bridas de plástico | Plastic ziptides | 4 |
| 4 | Catadrioptico | Reflector | 1 |
| 5 | Desplazador catadrioptico | Support for reflector | 1 |
| 6 | Tornillos M5x10 ISO7380 | M5x10 fasteners ISO7380 | 2 |
| 7 | Tuercas M5 DIN6923 | M5 Nut DIN6923 | 2 |
| 8 | Luz portamatriculas | License support light | 1 |

FIGURA 1 / FIGURE 1

FIGURA 2 / FIGURE 2

FIGURA 3 / FIGURE 3